A coil has an inductance, ( L ) of one Henry, ( 1H ) when the current flowing through the coil changes at a rate of one ampere/second, ( A/s ). This change induces a voltage of one volt, ( UL ) in it.
U_L=-L{di} over {dt}	(1)

'di' is difference in current, 'dt' is difference in time. So measure both at the start (usually when its at zero), then measure second time at it's peak and you get change in current per unit of time. But this can be calculated from frequency alone. The voltage and current are not meant to be the rms values, so if you need 28V rms, you need to convert that into peak voltage to get actual value in time.

Inductors are devices that can store their energy in the form of a magnetic field. Inductors are made from individual loops of wire combined to produce a coil and if the number of loops within the coil are increased, then for the same amount of current flowing through the coil, the magnetic flux will also increase.
So by increasing the number of loops or turns within a coil, increases the coils inductance. Then the relationship between self-inductance, ( L ) and the number of turns, ( N ) and for a simple single layered coil can be given as:

L=N{%phi} over {I}	(2)

Φ is the magnetic flux,

%phi=B x A	(3)

B is the flux density, and A is the area.

Magnetic flux density is higher when we have more turns, lower if the turns are over bigger area and higher when more current is flowing. Also higher with higher "relative magnetic permiability" of the core around which the coil is wound.

B=%mu_0 N*I over l	(4)

μο is the Permeability of Free Space (4.π.10-7)
A is the Inner Core Area (2π r) in m^2
 ℓ is the length of the Coil in metres
Then by substituting B in the first equation for L will give us:

L=%mu_0 N^2*A over l	(5)

In my case I need a transformer with secondary current of 48.9A, but voltage 28V rms at 50Hz

First we need to work with numbers for peak current and peak voltage:

U_P = U_RMS × √2	(6)

peak voltage UP = 39.59V
peak current IP = 69.01A

Now we need to work out the time difference which will get us the inductance according the first formula above.

In a coil, current is 90 degrees behind voltage, but the shift itself doesn't matter. But we're talking about sin(x) and -cos(x) functions, so for current say -cos(pi/2) = 0 and -cos(pi) = UP, so time difference to reach full voltage is pi/2. 50Hz means that 2pi = 1/50, so pi/2 = 1/200s. Now we can use the first fomula

V_L=-L{di} over {dt} rightarrow newline L {di} over {dt} =- V_L rightarrow newline L =- V_L dt over di rightarrow newline L = -39.59 (1/200) over 69.01 = -0.0028684H = -2.8684 mH	(7)

The sign of the mH does not matter so I'll work with positive 2.8684mH

At this point I needed to dive more into ferrite cores and found this equation.
N = sqrt {L over A_L}	(8)

AL is inductance factor of a core, so it's crutial to find one with high inductance factor because I want low number or turns. This calculator contains real materials to choose from:
https://coil32.net/online-calculators/amidon-ferrite-torroid-calculator.html

Optional: Or when choosing a core we can try this calculator to maybe find out what loop diameter would be just right for a core, but I found that choosing from existing materials was quicker.

Material number 77 is used for transformers, with dimentions FT-290 and L = 2.86mH gave me only 28 number of turns which is perfect. This also gave me a value of 2000 for "Initial magnetic permeability (μ)"

Now the value of 2.8684mH is a result of magnatic flux of the primary winding. Plugging all values here resulted in 30 turns on the secondary.
https://coil32.net/online-calculators/ferrite-torroid-calculator.html

input:
L = 2.8684mH
OD=73.7mm
ID=38.9mm
h=12.7mm
chamfer = 1mm (guess)
mu_r = 2000 relative magnetic permiability
d= Wire diameter, selected 10AWG because it's maximum current is 55A

http://hyperphysics.phy-astr.gsu.edu/hbase/Tables/wirega.html
Output:
N = 29.755
AL = 3,240 uH/N2
lw = 1.791 meters of wire

This means I only need 2 meters of 10AWG wire to make only 30 turns, given this particular core. But I need to point out that this is probably inaccurate because we calculated this based on a bare core, not based on the primary winding on this core. But it gave me an idea what number of turns I can plug in next. But experimentally I might need less turns if the wire gets too big and messy so maybe I'll try different results for say 25-30.

So back to equation (2), we can calculate magnetic flux needed to be created by the primary winding. I'm plugging in secondary turns, secondary inductance, secondary current – should give me required flux.

%phi={L*I} over {N} rightarrow newline %phi=0.0028684H * 48.9A over 30 = 0.004675492
Now if we can calculate the inductance for the primary coil, then given magnatic flux we maybe able to try to see how many turns it'll be using formula (2).

This was for the secondary winding. Now I need the primary winding.

Because we're working with 48.8A and 28V, that means the transformer operates at 1,369W of power (P). Given the voltage of 230V, the primary current will need to be

I_1=1369 over 240=5.7 A_rms newline I_peak = sqrt{2} * 5.95 = 8.42 A_peak newline U_peak = sqrt{2} * 230 = 325.2 V_peak	(9)

As before the T = 1/200s so required inductance of primary coil is:

L =- V_L dt over di rightarrow newline L = -325.2 (1/200) over 8.42 = -0.0028684H = -193.1116 mH	(10)

L = 193.1 mH

N={L*I} over {%phi} rightarrow newline N=0.1931H*5.7A over 0.004675492 = 235 turns!
Independent second way of calculating confirms my results exactly!?

Wire size chosen is 20AWG because that can take 11A of current.

This core actually has the same properties as in my equations!
https://www.mouser.co.uk/ProductDetail/Fair-Rite/5977011101?qs=mU1%2Fij5TiH5UxMFyMMr8sA%3D%3D

Recalculating all values using the online calculator gives me AL = 3243 nH/N^2 which doesn't agree with datasheet. So I tweaked the μR to final value 2159. Then the result showed the same AL as from the datasheet – because tweaking this also affected sligtly the final number of turns and the wires lengths.

Primary:	Secondary:
N = 235 turns / l = 15 meters of wire	N = 29 turns / l = 1.72 meters of wire

Core: £32.23 with shipping and vat
Wire primary: £12.20 GBP with shipping and vat
Wire secondary: $21.89 with shipping and vat

Winding

Primary turns: 235
Wire area: 0.5027 sqmm
Wire radius: r = sqrt(A/pi); r = 0.4mm
ID = 38.9mm
Coil circumference:
O = (ID – r/2) *2 * pi; O = 243.159 mm

Turns first layer: Nr1 = O/(r*2); Nr1 = 303.9

This means only one layer will be needed, I'll just space it as closely as possible and then maybe adjust. I should've bought a smaller core, that's crazy how efficient the core makes it unless I made a mistake because it looks too good.

--
After having this prototype built, I'm getting a terrible inrush currents. These are calculated using DC formulas.

Copper resistivity of 20AWG is 0.0333ohm per meter. We have 15m, so 0.4995ohms, that is 480A.
I tried to limit them using 4x "AS32 20010" limiters but unsuccessfully, they heat up within about 1/2 second and immediately tripped a B20 circuit breaker which was set up to protect the current limiters from exceeding their maximum current.

If I increase number of turns on the primary, what will happen? Hard to answer. I can try to require a higher flux, and see what happens with the turns, but even that depends on turns on the secondary. So what happens when we choose less turns on secondary? Will the required flux go up so the number of turns should go up I think.

%phi={L*I} over {N} rightarrow newline %phi=0.1931H*5.7A over 400 =